## Slide 1: CDH Subsystem Testing Overview
Communication testing (done) –
Mission : Ensure that data transmission is successful between pair of Xbee.
Test conditions : Done by connecting both Xbee to separate laptops and data was sent via comm operator after configuring them using
XCT-U .
Pass/Fail Criteria : Take considerable no. of observations and verify correctness.
Conclusion – Pass.
Range Testing (being done) –
Mission : To get desirable range.
Test conditions : to be done in a large ground/road so as to give us range of about 1.5 Km.
Pass/Fail criteria : Take observations, rotate antenna, vibrate and observe the range till which communication link is not broken.

## Slide 2: FSW Testing Overview
FSW testing (To be done) –
Mission : Ensure correct accumulation of data from
sensors and synchronous transmission and termination of
data . Handle processor reset.
Test bed : Software is developed in C and compiled using AVRgcc.
Pass/Fail criteria : FS must be able to gather data from various sensors and store as well as transmit it to the GCS. Smooth transmission achievement.
Status : Accumulation of data from sensors except GPS is tested(i.e., getting values through ADC) and UART interface is also tested for microcontroller. Rest is yet to be developed.

## Slide 3: GCS Testing Overview
GCS software testing –
Mission : Correctness of GCS software.
Test bed : Matlab was used to acquire data from USB port and process it to plot real time graphs for voltage, temperature, altitude and other data.
Status – Artificially generated packets were sent to GCS and it was observed that plots and information are correctly updated in figure and stored correctly in csv file.