## Slide 1: Temperature measure using thermocouples
Thermocouple :
A thermocouple is a device consisting of two different conductors (usually metal alloys)
that produce a voltage, proportional to a temperature difference, between either
end of the two conductors. Thermocouples are a widely used type of temperature sensor
for measurement and control and can also be used to convert a temperature gradient
into electricity. They are inexpensive,[ interchangeable, are supplied with standard
connectors, and can measure a wide range of temperatures. In contrast to most other
methods of temperature measurement, thermocouples are self powered and require
no external form of excitation. The main limitation with thermocouples is accuracy and
system errors of less than one degree Celsius (C) can be difficult to achieve.

## Slide 2
Because of the temperature difference between junction end and tail end a voltage
difference can be measured between the two thermoelements at the tail end: so the thermocouple is a temperature-voltage transducer.
emf = T2ʃT1 S12 dT = T2ʃT1 (S1-S2) dT;
T1 the reference temp. and T2 the measuring temperature.
S12 is the seebeck coefficient of thermocouple and s1 and s2 are the
seebeck coefficients of individual thermoelements.
The circuit is as follows:
AD590:
The AD590 is a two-terminal integrated circuit temperature
transducer that produces an output current proportional to
absolute temperature. For supply voltages between +4 V and
+30 V the device acts as a high impedance, constant current

## Slide 3
regulator passing 1 µA/K. Laser trimming of the chip’s thin-film
resistors is used to calibrate the device to 298.2 µA output at
298.2K (+25°C).
The reason for using AD590 is that room temperature need not be always 25˙C
So the AD590 ensures the current flow proportional to absolute temp. so if temp. is
30˙C a current of 30μA flows and measures the voltage across a resistor corresponding to that temperature.
TO maintain fixed reference voltage Of 2.5volt AD580 is used
Vmeasured = Vjunction – Vref + Vr1
where Vr1 is the voltage corresponding to room temperature and the temperature
Of the junction is measured by using the seebeck law that
Vjunction – Vref = K( Tjunction – Tref )
Cold junction compensation if done maintains lower junction at a fixed temp.
Then a different circuit may be used.

## Slide 4
The reading of the measurement are as follows:
voltage (measured in mv) Temperature
26 200
29 250
31 300
33 350
34 400
36 450
37 480
Temperature of the junction was maintained using a solder iron whose temperature can be controlled .