## Slide 1
Computer on FPGA
Faculty Guide: Shubhajit Roy Chowdhury
Students: Jashwanth Reddy
  Kurra Lokesh

## Slide 2: What is FPGA??
It’s a Programmable Logic Device.
Contains logic blocks and interconnects.
These blocks contain memory , logic ,math functions etc…..
I/O blocks
SRAM cells pathway decide functionality i.e., LUT
EEPROM cells – Non-volatile but programmable

## Slide 3: VHDL FPGA
Model for hardware device
Design
  Entity & Signals
  Architecture
  Configuration
Programming language
  Procedures
  Functions

## Slide 4: Simple VHDL Program
library ieee; Use ieee.std_logic_1164.all; entity counter is port( clk: in std_logic; reset: in std_logic; enable: in std_logic; count: out std_logic_vector (3 downto 0)); end counter; architecture behav of counter is signal pre_count: std logic_vector (3 downto 0); begin process( clk , enable, reset) begin if reset = '1' then pre_count <= "0000"; | Elsif (clk='1' and clk'event) then if enable = '1' then pre_count <= pre_count + "1"; end if; end if; end process; count <= pre_count; end behav;

## Slide 5: Simulation Results

## Slide 6: FPGA
DE1 board
State of art Cyclone II 2C20.
For simple Digital Logic experiments it contains slides , switches, LED’s etc…

## Slide 7: Supporting softwares
Quartus II web Edition
Nios II Software Build Tools
SOPC builder
Nios II Embedded Design Suite
Modelsim Altera Starter Edition 6.5b

## Slide 8: Problem!!!

## Slide 9: Small Demo

## Slide 10: Experiments
Audio Signals
  24bit CODEC
Video Signal
  VGA Connector
  PS2 connector was not available for connectivity.
  However we tested VGA connector

## Slide 11: How to run on FPGA
First we created a new project.
We added required vhdl files to the project.
Compile Design consists of
  Analysis & Synthesis
    I/O Assignment Analysis
  Place and Route
  Assembler
  TimeQuest Analysis

## Slide 12: How to Dump on FPGA
After compiling vhdl code go to Assignment->pin planner and give required pins on FPGA. Perform I/O Analysis and open tools->programmer-> and finally configure .sof file and dump into FPGA.

## Slide 14: Basic Module

## Slide 15: NIOS-II processor
Soft processor that can be instantiated on Altera FPGA device.
Provide timers , communication interfaces , i/o interfaces , memories etc…
Follows RISC Architecture.

## Slide 16
One can spend life time to learn these FPGA architectures and their development.

## Slide 17
THANK YOU