## Slide 1: Computer systems Organization
Memory Hierarchies -- Spring 2010 -- IIIT-H -- Suresh Purini

## Slide 2
Source: Dave Patterson

## Slide 3: Desired Features for Memory
Memory should be
Large – So that programs with huge memory footprint can be executed.
Fast – Why?
However, in real world these two are contradictory requirements!

## Slide 4: Random Access Memory (RAM)
Main memory can be logically viewed as an array of bytes
In RAMs, time taken to access any byte of memory is exactly same.
  Compare this against Disks, Magnetic Tapes, CD-Rom
Technologies for RAM
  Static RAM (SRAM)
    Low density, high power, expensive, fast
    Static: content will last “forever”
  Dynamic RAM (DRAM)
    High density, low power, cheap, slow
    Dynamic: need to be “refreshed” regularly
Main Memory – DRAM
Cache – SRAM

## Slide 5: Random Access Memory (RAM) Technology
Why do computer designers need to know about RAM technology?
  Processor performance is usually limited by memory bandwidth
  As IC densities increase, lots of memory will fit on processor chip
  Tailor on-chip memory to specific needs
    Instruction cache
    Data cache
    Write buffer
What makes RAM different from a bunch of flip-flops?
  Density: RAM is much more denser

## Slide 7: Static RAM
SRAM stores each bit in a bistable memory cell
Each cell is implemented with a six transistor circuit
The above circuit can stay in one of two possible states indefinitely (as long as the circuit is powered)
    Low density, high power, expensive, fast
    Static: content will last “forever”

## Slide 8: Dynamic RAM (DRAM)
DRAM stores each bit as a charge on a capacitor.
DRAM storage can be made very dense
DRAM cell will lose its charge within a time period of around 10 to 100 milliseconds
Memory system should be periodically refreshed by reading every bit of memory and writing it back
    High density, low power, cheap, slow
    Dynamic: need to be “refreshed” regularly

## Slide 9: SRAM vs DRAM

## Slide 10: The Illusion of Fast and Large Memories
SRAMs – For small but fast Cache Memories
DRAMs – For large but slow Main Memories
Design Goal for Memory Hierarchy: Give the illusion of large and fast memory
Key Idea: Exploit temporal and spatial locality of the programs to achieve the illusion.

## Slide 11: Principle of Locality of Reference
The Principle of Locality:
  Program access a relatively small portion of the address space at any instant of time.
Two Different Types of Locality:
  Temporal Locality (Locality in Time): If an item is referenced, it will tend to be referenced again soon.
  Spatial Locality (Locality in Space): If an item is referenced, items whose addresses are close by tend to be referenced soon.

## Slide 12: Principle of Locality
Function sumvec exhibits
Good temporal locality w.r.t variable sum
Good spatial locality w.r.t variable v (Stride-1 reference pattern)
Spatial locality decreases for Stride-k reference patterns as k increases
N = 8
Hey how about locality of instruction fetches?
Loops exhibit good temporal and spatial locality

## Slide 13: Principle of Locality
Does the function sumarrayrows exhibit good spatial locality?
What is the Stride for the array variable a?
M = 2
N = 3

## Slide 14: Principle of Locality
Does the function sumarraycolumns exhibit good spatial locality?
What is the Stride for the array variable a?
M = 2
N = 3

## Slide 15
Memory Hierarchy

## Slide 16: Basic Principle of Caching in the Memory Hierarchy
Focus of this lecture:
Level k: on-chip cache memory (SRAM)
Level k+1: Main memory (DRAM)

## Slide 17: What is a Cache Hit and Cache Miss?
Let us say
Cache size – 128 bytes (27 bytes)
Cache line/block size – 32 bytes
Main Memory 512 bytes (29 bytes)
Main memory is also logically divided into 24 blocks each of size 32 bytes
When the processor accesses a word of memory
Cache hit: If the block containing the word is available in the Cache
Cache Miss: If the block containing the word is not available in Cache
Question: How to search the cache for the block containing the word of memory the processor is accessing?

## Slide 18: What happens on a Cache Miss?
The block containing the word of memory has to be fetched into the cache.
We may have to overwrite an existing block if the cache is already full. This is called replacing or evicting the block.
Question: Which block should we evict? (Cache’s Replacement policy)
  Random replacement policy, Least Recently Used (LRU) replacement policy, FIFO, Least Frequently Used (LFU), ….

## Slide 19
Block No | Main Memory
0000 | 
0001 | 
0010 | 
0011 | 
0100 | 
0101 | 
0110 | 
0111 | 
1000 | 
1001 | 
1010 | 
1011 | 
1100 | 
1101 | 
1110 | 
1111 | 
Main Memory = 16 32-byte blocks
Cache = 4 32-byte blocks
Index | Valid Bit | Tag | Data
00 | N |  | 
01 | N |  | 
10 | N |  | 
11 | N |  | 
Tag | Index | Byte Offset
Cache Structure
Memory Address
Block K of memory is mapped to the block K mod 4 of cache.
Direct-Mapped Cache Organization

## Slide 20: Direct Mapped Cache Organization
What is the Hit rate for the following loop assuming the cache is initially empty? Assume the array A is allocated memory starting at address 0. Also assume the variable sum is located in a register.
Hit Rate: Percentage of memory references served from the cache
Miss Rate: 1 – Hit Rate
for( i = 0; i < 128; ++i)
sum = sum + A[i] ;
Three types of Cache Misses
Compulsory or Cold Start Misses
Conflict Miss
Capacity Miss

## Slide 21: Conflict Misses and Direct Mapped Cache Organization
What is the Hit rate for the following loop assuming the cache is initially empty? Assume the array A is allocated memory starting at address 0. Also assume the variable sum is located in a register.
for( i = 0; i < 128; i = i + 32)
sum = sum + A[i] ;
for( i = 0; i < 128; i = i + 32)
A[i] = ~A[i] ;
Hmm! Unnecessary Cache Misses in the second for loop. Conflict Misses? How can we solve this problem.

## Slide 22: Conflict Misses and Direct Mapped Cache Organization
What is the Hit rate for the following loop assuming the cache is initially empty? Assume array x is allocated memory starting at address 0x0 and array y is allocated memory starting at address 0b010000000.
Variables sum and i are located in registers
float dotprod(int x[8], int y[8])
{
int sum = 0, i ;
for( i = 0; i < 8; ++i )
sum = sum + x[i] * y[i] ;
return sum;
}

## Slide 23: Direct Mapped Cache Organization
By looking at this picture can you guess ….
Memory size
Block size
No of blocks in main memory
How many distinct main memory blocks can map to the same cache block?

## Slide 24
Block No | Main Memory
0000 | 
0001 | 
0010 | 
0011 | 
0100 | 
0101 | 
0110 | 
0111 | 
1000 | 
1001 | 
1010 | 
1011 | 
1100 | 
1101 | 
1110 | 
1111 | 
Main Memory = 16 32-byte blocks
Cache = 4 32-byte blocks
Valid Bit | Tag | Data
N |  | 
N |  | 
N |  | 
N |  | 
Tag | Byte Offset
Cache Structure
Memory Address
Block K of memory can be placed anywhere in Cache.
Fully Associative Cache Organization

## Slide 25: Conflict Misses and Fully Associative Cache Organization
What is the Hit rate for the following loop assuming the cache is initially empty? Assume the array A is allocated memory starting at address 0. Also assume the variable sum is located in a register.
for( i = 0; i < 128; i = i + 32)
sum = sum + A[i] ;
for( i = 0; i < 128; i = i + 32)
A[i] = ~A[i] ;
No Conflict Misses at all!
In Real Life: It is extremely expensive to build fast Tag Lookup hardware.

## Slide 26: Fully Associative Cache Organization
What is the Hit rate for the following loop assuming the cache is initially empty? Assume array x is allocated memory starting at address 0x0 and array y is allocated memory starting at address 0x010000000.
Variables sum and i are located in registers
float dotprod(int x[8], int y[8])
{
int sum = 0, i ;
for( i = 0; i < 8; ++i )
sum = sum + x[i] * y[i] ;
return sum;
}

## Slide 27: Set Associative Cache Organization

## Slide 28: Set Associative Cache Organization

## Slide 29: Typical Multi-Level Cache Organization

## Slide 30: Average Memory Access Time
Average Memory Access Time =
Cache Memory Access Time * Hit Ratio + (1 – Hit Ratio)* Miss Penalty
Miss Penalty: (roughly) Time taken to access the main memory block and put it in the cache.

## Slide 31: Memory Wall
Technology Trends

## Slide 32: Memory Wall