## Slide 1: Computer systems Organization
Input/Output -- Spring 2010 -- IIIT-H -- Suresh Purini

## Slide 2: The Big Picture: Where are we now?
Input and Output

## Slide 3
Memory
CPU
S
Y
S
T
E
M
B
U
S
Keyboard
Monitor
Hard Disk
Printer
Keyboard
Controller
Graphics
Controller
Hard Disk
Controller
Printer
Controller
High level view of connections between various modules in a computer system

## Slide 4
System Bus Consists of:
Address lines
Data lines
Control lines
Typical Control Lines:
Memory write
Memory read
I/O write
I/O read
Transfer ACK
Bus request
Bus grant
Interrupt request
Interrupt ACK
Clock

## Slide 5: Typical Signal Lines for Memory and CPU

## Slide 6
Traditional Bus Architecture

## Slide 7
Another Possible Bus Architecture

## Slide 8: Typical Signal Lines for I/O Modules (Device Controllers)
Memory
CPU
Device
Controller
Device
Data
Address
Control
Interrupt
Data
Control
Status

## Slide 9: Typical Signal Lines for I/O Modules (Device Controllers)
Memory
CPU
Device
Controller
Device
Data
Address
Control
Interrupt
Data
Control
Status
We need a device drive which knows how to interface with the Device Controller

## Slide 10: Floppy Disk Controller
Floppy disk
Controller
FDD 0
FDD 1
Control Signal | Action by the device
Drive Select | FDD gets logically connected
Head Select | FDD selects either the top or bottom head
Direction | Indicate the direction of head movement (inward or outward)
Step | Move one track
…………….. | ………
Status Signal | Action by the device
Track 0 | Read/write head is positioned over the track 0
Write Protect | FDD is write protected
Ready | FDD is ready for operation
…………….. | ………

## Slide 11: Types of Data Transfer
Bus interconnection should support the folllowing types of transfer:
Memory to processors
Processor to memory
I/O to processor
Processor to I/O
I/O to or from memory (Direct Memory Access – DMA)

## Slide 12: Elements of Bus Design: Bus Type
Dedicated
  Separate data & address lines
Multiplexed
  Shared lines
  Address valid or data valid control line
  Advantage - fewer lines
  Disadvantages
    More complex control
    Ultimate performance

## Slide 13: Elements of Bus Design: Method of Arbitration
More than one module controlling the bus
  e.g. CPU and DMA controller
Only one module may control bus at one time
Arbitration may be Centralised (Bus Controller) or Distributed

## Slide 14: Elements of Bus Design: Timing
Co-ordination of events on bus
Synchronous
  Events determined by clock signals
  Control Bus includes clock line
  A single 1-0 is a bus cycle
  All devices can read clock line
  Usually sync on leading edge
  Usually a single cycle for an event
Asynchronous

## Slide 15: Timing of Synchronous Bus Operations
Important Remark: Bus clock and Processor clock are different.

## Slide 16: Timing of Asynchronous Bus Operations

## Slide 17: Timing of Asynchronous Bus Operations

## Slide 18: Various Bus Protocols
Industry Standard Architecture – ISA (1982)
Extended Industry Standard Architecture – EISA
Vesa Local Bus – VL Bus
Peripheral Component Interconnect – PCI (Early 1990s)

## Slide 19: Typical Desktop System