## Slide 1: Computer systems Organization
Input/Output -- Spring 2010 -- IIIT-H -- Suresh Purini
ACK: Some of these slides are based on Stallings

## Slide 2: The Big Picture: Where are we now?
Input and Output

## Slide 3
Memory
CPU
S
Y
S
T
E
M
B
U
S
Keyboard
Monitor
Hard Disk
Printer
Keyboard
Controller
Graphics
Controller
Hard Disk
Controller
Printer
Controller
High level view of connections between various modules in a computer system

## Slide 4
System Bus Consists of:
Address lines
Data lines
Control lines
Typical Control Lines:
Memory write
Memory read
I/O write
I/O read
Transfer ACK
Bus request
Bus grant
Interrupt request
Interrupt ACK
Clock

## Slide 5: Basic Components of a Computer and their Interconnection

## Slide 6: Input/Output Problems
Wide variety of peripherals
  Delivering different amounts of data
  At different speeds
  In different formats
All slower than CPU and RAM
Need I/O modules (with their Device Drivers and the corresponding Operating System support)

## Slide 7: I/O Device Interface
Interface to CPU and Memory
Interface to one or more peripherals

## Slide 8: I/O Device Interface
Interface to CPU and Memory
Interface to one or more peripherals

## Slide 9: I/O Module Functions
Control & Timing
CPU Communication
Device Communication
Data Buffering
Error Detection

## Slide 10: I/O Steps
CPU checks I/O module device status
I/O module returns status
If ready, CPU requests data transfer
I/O module gets data from device
I/O module transfers data to CPU
Variations for output, DMA, etc.

## Slide 11: I/O Decisions
Hide or reveal device properties to CPU
Support multiple or single device
Control device functions or leave for CPU

## Slide 12: Input Output Techniques
Programmed I/O
Interrupt driven
Direct Memory Access (DMA)

## Slide 13: Programmed I/O
CPU has direct control over I/O
  Sensing status
  Read/write commands
  Transferring data
CPU waits for I/O module to complete operation
Wastes CPU time

## Slide 14: Programmed I/O - detail
CPU requests I/O operation
I/O module performs operation
I/O module sets status bits
CPU checks status bits periodically
I/O module does not inform CPU directly
I/O module does not interrupt CPU
CPU may wait or come back later

## Slide 15
Programmed I/O

## Slide 16: I/O Mapping
Memory mapped I/O
  Devices and memory share an address space
  I/O looks just like memory read/write
  No special commands for I/O
    Large selection of memory access commands available
Isolated I/O (I/O Mapped I/O)
  Separate address spaces
  Need I/O or memory select lines
  Special commands for I/O
    Limited set

## Slide 17: Interrupt Driven I/O
Overcomes CPU waiting
No repeated CPU checking of device
I/O module interrupts when ready

## Slide 18: Interrupt Driven I/O Basic Operation
CPU issues read command
I/O module gets data from peripheral whilst CPU does other work
I/O module interrupts CPU
CPU requests data
I/O module transfers data

## Slide 19
Interrupt Driven I/O

## Slide 20: CPU Viewpoint
Issue read command
Do other work
Check for interrupt at end of each instruction cycle
If interrupted:-
  Save context (registers)
  Process interrupt
    Fetch data & store

## Slide 21
Interrupt Processing

## Slide 22: Design Issues
How do you identify the module issuing the interrupt?
How do you deal with multiple interrupts?
  i.e. an interrupt handler being interrupted

## Slide 23: Identifying Interrupting Module
Different line for each module
  PC
  Limits number of devices
Software poll
  CPU asks each module in turn
  Slow

## Slide 24: Identifying Interrupting Module
Daisy Chain or Hardware poll
  Interrupt Acknowledge sent down a chain
  Module responsible places vector on bus
  CPU uses vector to identify handler routi
  ne
Bus Master
  Module must claim the bus before it can raise interrupt

## Slide 25: Multiple Interrupts
Each interrupt line has a priority
Higher priority lines can interrupt lower priority lines
If bus mastering only current master can interrupt

## Slide 26: Example
80x86 has one interrupt line
8086 based systems use one 8259A interrupt controller
8259A has 8 interrupt lines

## Slide 27: Sequence of Events
8259A accepts interrupts
8259A determines priority
8259A signals 8086 (raises INTR line)
CPU Acknowledges
8259A puts correct vector on data bus
CPU processes interrupt

## Slide 28: PC Interrupt Layout
8086
INTR
8259A
IRQ0
IRQ1
IRQ2
IRQ3
IRQ4
IRQ5
IRQ6
IRQ7

## Slide 30: Taxonomy of Interrupts in Pentium
Software Interrupts are Synchronous Events whereas Hardware Interrupts are Asynchronous Events.

## Slide 31: Interacting with I/O Devices: MS-Dos on an x86 Machine

## Slide 32: Pentium Modes
Real Mode
Protected Mode

## Slide 33: Pentium

## Slide 34
Direct Memory Access

## Slide 35: I/O Techniques Summary
 | No Interrupts | Use of Interrupts
I/O-to-memory Transfer through Processor | Programmed I/O | Interrupt-driven I/O
Direct I/O-to-memory transfer |  | Direct Memory Access