## Slide 1: Review: Energy & Power Equations
E = CL VDD2 P01 + tsc VDD Ipeak P01 + VDD Ileakage
P = CL VDD2 f01 + tscVDD Ipeak f01 + VDD Ileakage
Dynamic power
(~90% today and decreasing relatively)
Short-circuit power
(~8% today and decreasing absolutely)
Leakage power
(~2% today and increasing)
f01 = P01 * fclock
Notes: f0->1 represents the energy consuming transition

## Slide 2: Power and Energy Design Space
 | Constant Throughput/Latency |  | Variable Throughput/Latency | 
Energy | Design Time | Non-active Modules |  | Run Time
Active | Logic Design Reduced Vdd Sizing Multi-Vdd | Clock Gating |  | DFS, DVS (Dynamic Freq, Voltage Scaling)
Leakage | + Multi-VT | Sleep Transistors Multi-Vdd Variable VT |  | + Variable VT
Notes: Physical capacitance: circuit style selection, transistor sizing, placement and routing, architectural optimizations.
input and output rise/fall times – determines short-circuit power
device thresholds and temperature – impacts leakage power
switching activity

## Slide 3: Bus Multiplexing
Share long data buses with time multiplexing (S1 uses even cycles, S2 odd)
S2
S1
D1
D2
S1
S2
D2
D1
Buses are a significant source of power dissipation due to high switching activities and large capacitive loading
  15% of total power in Alpha 21064
  30% of total power in Intel 80386
But what if data samples are correlated (e.g., sign bits)?

## Slide 4: Correlated Data Streams
Bit position
MSB
LSB
Bit switching probabilities
For a shared (multiplexed) bus advantages of data correlation are lost (bus carries samples from two uncorrelated data streams)
  Bus sharing should not be used for positively correlated data streams
  Bus sharing may prove advantageous in a negatively correlated data stream (where successive samples switch sign bits) - more random switching

## Slide 5: Glitch Reduction by Pipelining
Glitches depend on the logic depth of the circuit - gates deeper in the logic network are more prone to glitching
  arrival times of the gate inputs are more spread due to delay imbalances
  usually affected more by primary input switching
Reduce logic depth by adding pipeline registers
  additional energy used by the clock and pipeline registers
PC
Fetch
Decode
Execute
Memory
WriteBack
Instruction
MAR
MDR
I$
D$
clk
pipeline
stage
isolation
register
Notes: Five stage pipeline (originally for performance, but also helps with energy)

## Slide 6: Power and Energy Design Space
 | Constant Throughput/Latency |  | Variable Throughput/Latency | 
Energy | Design Time | Non-active Modules |  | Run Time
Active | Logic Design Reduced Vdd Sizing Multi-Vdd | Clock Gating |  | DFS, DVS (Dynamic Freq, Voltage Scaling)
Leakage | + Multi-VT | Sleep Transistors Multi-Vdd Variable VT |  | + Variable VT
Notes: Physical capacitance: circuit style selection, transistor sizing, placement and routing, architectural optimizations.
input and output rise/fall times – determines short-circuit power
device thresholds and temperature – impacts leakage power
switching activity

## Slide 7: Clock Gating
Gate off clock to idle functional units
  e.g., floating point units
  need logic to generate disable signal
    increases complexity of control logic
    consumes power
    timing critical to avoid clock glitches at OR gate output
  additional gate delay on clock signal
    gating OR gate can replace a buffer in the clock distribution tree
Most popular method for power reduction of clock signals and functional units
R
e
g
clock
disable
Functional
unit
Notes: Motorola’s Mcore numbers for number of pipeline latches disabled by clock gating on pipeline stall

## Slide 8: Clock Gating in a Pipelined Datapath
For idle units (e.g., floating point units in Exec stage, WB stage for instructions with no write back operation)
PC
Fetch
Decode
Execute
Memory
WriteBack
Instruction
MAR
MDR
I$
D$
clk
No FP
No WB

## Slide 9: Power and Energy Design Space
 | Constant Throughput/Latency |  | Variable Throughput/Latency | 
Energy | Design Time | Non-active Modules |  | Run Time
Active | Logic Design Reduced Vdd Sizing Multi-Vdd | Clock Gating |  | DFS, DVS (Dynamic Freq, Voltage Scaling)
Leakage | + Multi-VT | Sleep Transistors Multi-Vdd Variable VT |  | + Variable VT
Notes: Physical capacitance: circuit style selection, transistor sizing, placement and routing, architectural optimizations.
input and output rise/fall times – determines short-circuit power
device thresholds and temperature – impacts leakage power
switching activity

## Slide 10: Review: Dynamic Power as a Function of VDD
Decreasing the VDD decreases dynamic energy consumption (quadratically)
But, increases gate delay (decreases performance)
VDD (V)
tp(normalized)
Determine the critical path(s) at design time and use high VDD for the transistors on those paths for speed. Use a lower VDD on the other logic to reduce dynamic energy consumption.
Notes: Good design practice keeps drain diffusion areas as small as possible
Self-loading is when the intrinsic capacitance (diffusion capacitance) starts to dominate the extrinsic load formed by wiring and fanout.
Propagation delay of a CMOS inverter as a function of supply voltage (normalized wrt delay at 2.5V supply). While the delay is relatively insensitive to supply variations for higher values of VDD, a sharp increase can be observed starting around 2VT. This operation regions should be avoided for high performance! Increasing VDD also has reliability concerns - oxide breakdown, hot-electron effects - that enforce firm upper bounds on the supply voltage in deep submicron processes. Lowering VDD slows down the gate!

## Slide 11: Dynamic Frequency and Voltage Scaling
Intel’s SpeedStep
  Hardware that steps down the clock frequency (dynamic frequency scaling – DFS) when the user unplugs from AC power
    PLL from 650MHz  500MHz
  CPU stalls during SpeedStep adjustment
Transmeta LongRun
  Hardware that applies both DFS and DVS (dynamic supply voltage scaling)
    32 levels of VDD from 1.1V to 1.6V
    PLL from 200MHz  700MHz in increments of 33MHz
  Triggered when CPU load change is detected by software
    heavier load  ramp up VDD, when stable speed up clock
    lighter load  slow down clock, when PLL locks onto new rate, ramp down VDD
  CPU stalls only during PLL relock (< 20 microsec)
Notes: Always keeps clock frequency within limits required by VDD to avoid clock skew problems

## Slide 12: Dynamic Thermal Management (DTM)
Initiation Mechanism:
How do we enable technique?
Response Mechanism:
What technique do we enable?
Trigger Mechanism:
When do we enable DTM techniques?

## Slide 13: DTM Trigger Mechanisms
Mechanism: How to deduce temperature?
Direct approach: on-chip temperature sensors
  Based on differential voltage change across 2 diodes of different sizes
  May require >1 sensor
  Hysteresis and delay are problems
Policy: When to begin responding?
  Trigger level set too high means higher packaging costs
  Trigger level set too low means frequent triggering and loss in performance
Choose trigger level to exploit difference between average and worst case power
Notes: Average case power dissipation can often be much lower than worst case due to
  Aggressive clock gating
  Applications variations
  Underutilized resources
    Not enough ILP
Currently about a 30% difference
Likely to further diverge…

## Slide 14: DTM Initiation and Response Mechanisms
Operating system or microarchitectural control?
  Hardware support can reduce performance penalty by 20-30%
Initiation of policy incurs some delay
  When using DVS and/or DFS, much of the performance penalty can be attributed to enabling/disabling overhead
  Increasing policy delay reduces overhead; smarter initiation techniques would help as well
Thermal window (100Kcycles+)
  Larger thermal windows “smooth” short thermal spikes

## Slide 15: DTM Activation and Deactivation Cycle
Trigger
Reached
Response Delay – Invocation time (e.g., adjust clock)
Response
Delay
Policy Delay – Number of cycles engaged
Policy
Delay
Check
Temp
Check
Temp
Turn
Response On
Initiation
Delay
Initiation Delay – OS interrupt/handler
Shutoff
Delay
Turn
Response Off
Shutoff Delay – Disabling time (e.g., re-adjust clock)

## Slide 16: DTM Savings Benefits
Time
Temperature
DTM Disabled
DTM/Response Engaged
Designed for cooling capacity without DTM
DTM trigger
level
Designed for cooling
capacity with DTM
System
Cost Savings

## Slide 17: Power and Energy Design Space
 | Constant Throughput/Latency |  | Variable Throughput/Latency | 
Energy | Design Time | Non-active Modules |  | Run Time
Active | Logic Design Reduced Vdd Sizing Multi-Vdd | Clock Gating |  | DFS, DVS (Dynamic Freq, Voltage Scaling)
Leakage | + Multi-VT | Sleep Transistors Multi-Vdd Variable VT |  | + Variable VT
Notes: Physical capacitance: circuit style selection, transistor sizing, placement and routing, architectural optimizations.
input and output rise/fall times – determines short-circuit power
device thresholds and temperature – impacts leakage power
switching activity

## Slide 18: Speculated Power of a 15mm mP

## Slide 19: Review: Leakage as a Function of Design Time VT
Reducing the VT increases the sub-threshold leakage current (exponentially)
But, reducing VT decreases gate delay (increases performance)
Determine the critical path(s) at design time and use low VT devices on the transistors on those paths for speed. Use a high VT on the other logic for leakage control.

## Slide 20: Review: Variable VT (ABB) at Run Time
VT = VT0 + (|-2F + VSB| - |-2F|)
where VT0 is the threshold voltage at VSB = 0
VSB is the source-bulk (substrate) voltage
 is the body-effect coefficient
VSB (V)
VT (V)
For an n-channel device, the substrate is normally tied to ground
A negative bias causes VT to increase from 0.45V to 0.85V
Adjusting the substrate bias at run time is called adaptive body-biasing (ABB)
Notes: Value of VGS where strong inversion occurs is VT
VSB is the source to bulk (body) or substrate bias (note relationship to body effect)
For tox = 5 nm then Cox = 7fF/micron^2 (typical tox less than 10nm (==100 angstroms) in today’s technology)
Typical values for NA = 10**15 atoms/cm**3 and ND = 10**16 atoms/cm**3
Observe that the threshold voltage has a positive value for a normal NMOS device and a negative for a normal PMOS device